# General Capability Description
E4D executes according to one of several run modes chosen by the user. Run modes can be classified generally as mesh generation modes, forward run modes, static inversion modes, and time-lapse inversion modes. Required input files, and the formats of those files, vary somewhat depending on the run mode. Refer to the online user guide for complete information.
Run Mode	Previous Designation*	Function	Description
ERT0	0	ER Test input	Validates input files for ERT run modes
ERT1	1	ER Mesh Generation Mode	Mesh generation for electrical resistivity modeling and inversion
ERT2	2	ER Forward Run Mode	Direct current potential field and electrical resistivity survey simulation
ERTAnalytic	‘analytic’	ER Forward Run Mode	Direct current potential field and electrical resistivity survey simulation (analytic solution)
ERT3	3	ER Static Inversion Mode	Electrical resistivity inversion for a single survey
ERT4	4	ER Time-lapse Inversion Mode	Electrical resistivity inversion for multiple time-lapse surveys
ERT5	5	Real-time (autonomous) / ER Time-lapse Inversion Model	Electrical resistivity inversion for real-time surveys
SIP0	N/A	SIP test input	Validates input files for SIP run modes
SIP1	21	SIP Mesh Generation Mode	Mesh generation for spectral induced polarization modeling and inversion
SIP2	22	SIP Forward Run Mode	Complex potential field and spectral induced polarization survey simulation
SIP3	23	SIP Static Inversion Mode	Spectral induced polarization inversion for a single survey
SIP4	24	SIP Multi-frequency Inversion Mode	Spectral induced polarization inversion for multiple-frequency surveys
ERTtank0	N/A	ERT Tank test input	Validates input files for ERT tank run modes
ERTtank1	31	ER Tank Mesh Generation Mode	Mesh generation for electrical resistivity modeling and inversion within a tank
ERTtank2	32	ER Tank Forward Run Mode	Direct current potential field and electrical resistivity survey simulations for tank scale imaging
ERTtank3	33	ER Tank Static Inversion Mode	Electrical resistivity inversion for a single survey within a tank
ERTtank4	34	ER Tank Time-lapse Inversion Model	Electrical resistivity inversion for multiple time-lapse surveys within a tank
ERTtank5	35	Real-time (autonomous) / ER Tank Time-lapse Inversion Model	Electrical resistivity inversion for real-time surveys
SIPtank0	N/A	SIP Tank test input	Validates input files for SIP tank run modes
SIPtank1	41	SIP Tank Mesh Generation Mode	Mesh generation for spectral induced polarization modeling and inversion within a tank
SIPtank2	42	SIP Tank Forward Run Mode	Complex potential field and spectral induced polarization survey simulations for tank scale imaging
SIPtank3	43	SIP Tank Static Inversion Mode	Spectral induced polarization inversion for a single survey within a tank
SIPtank4	44	SIP Tank Multi-frequency Inversion Mode	Spectral induced polarization inversion for multiple-frequency surveys within a tank