## SIP Mesh Generation Tank Tutorial

Note: This example is the based on the files in mode_ERTtank1/two_blocks. The generated mesh files will be the same as in this example EXCEPT the two_blocks.sig file, which will contain two columns, the real conductivty and imaginary conductivity as specified in the .cfg file.
The mesh files (.1.ele, .1.node, .1.face, .1.edge, .trn) generated in mode ERTtank1 can be used for forward and inverse modeling.
### Run mode SIPtank1 is provided as a convenient way to generate a conductivity file (.sig).
### Conceptual Diagram
In this example, we build a mesh of a laboratory tank as shown in Figure 1. This example can be found in the jupyter notebook SIPtank1.ipynb. The notebook clear_files.ipynb clears all files generated before running SIPtank1.pynb.
In the run mode SIP1 example (mode_SIP1) the defined surface boundaries (flag=2) were far enough away from the electrode locations such that these boundaries did not influence the data; surface boundaries were defined in mode SIP1 as having zero potential. In contrast, in a laboratory tank, the tank boundaries are close enough to the electrodes to influence the data. Therefore in run mode ERTtank1, surface boundaries (i.e. tank boundaries) (flag=2) are computationally equivalent to defining a zero flux boundary.
The other difference in a laboratory tank is a ghost node must be defined to use the mesh in the forward and inverse modeling run modes. E4D simulates potentials by solving for the pole solution at each electrode and subtracting the potential generated by the current sink electrode. For example, the total potential Pt between electrode A and B is solved as:
Pt=PA-PB
However, the tank boundaries prevent computing the solution of PA and PB directly, so a ghost node is used which serves as the current sink electrode for every pole solution. Since the same ghost sink is used for every electrode pole solution, the effects of the sink cancel out when the potential from the current sink is subtracted from the potential from the current source. In modes ERTtank1 and SIPtank1, the total potential Pt between electrode A and B, where the ghost sink is Pg is computed as:
Pt=(PA-Pg)-(PB-Pg)

Figure 1: The schematic of the laboratory tank mesh used in this example.

### Building the Mesh
In addition to the mesh configuration file, the run configuration file e4d.inp is needed to build the mesh. In mode ERTtank1, the only file that must be listed is the mesh configuration file. The run configuration file for this example is shown below.
<begin run configuration file e4d.inp> (this line is not included in the file)
SIPtank1
tank.cfg
<end run configuration file e4d.inp> (this line is not included in the file)
To build the mesh, execute the command:
<e4d_dir>/bin/mpirun -np 1 <e4d_dir>/bin/e4d
or
mpirun -np 1 e4d
if <e4d_dir>/bin is in the executable path, where <e4d_dir> is the E4D installation directory. E4D builds the input files for triangle and tetgen, and calls each to build the mesh. E4D then builds a conductivity file for the mesh as specified in the mesh configuration file, and calls px to build a file for visualization. The files generated include:
File	Generated by	Description
tank.poly	e4d	Tetgen input file generated by E4D. Not used in run modes > 1.
tank.1.node	tetgen	Tetgen node file. Gives the nodal coords of the mesh.
tank.1.ele	tetgen	Tetgen element file. Describes how nodes are connected to form elements.
tank.1.face	tetgen	Tetgen face file. Describes which nodes form boundary faces.
tank.1.neigh	tetgen	Tetgen neighbor file. Provides neighbors of all elements.
tank.sig	e4d	Conductivity file. Describes element real and imaginary conductivities and is written to the visualization file.
tank.xmf / tank.h5	px	Xdmf files used to visualize mesh and conductivity distribution.
tank.exo	bx	Exodus file used to visualize mesh and conductivity distribution.

<begin file tank.cfg> this line is not included in tank.cfg

1.3 1e12 mesh quality (m_qual) max volume (max_evol_def)
0.0 bottom of mesh elevation (m_bot)
1 flag to build mesh (tet_build_flag)
"tetgen" command to run tetgen (tet_loc)
"triangle" command to run triangle (tri_loc)
149
1	0.000	0.000	0.500	2 boundary points
2	0.025	0.000	0.500	2
3	0.050	0.000	0.500	2
4	0.075	0.000	0.500	2
5	0.100	0.000	0.500	2
6	0.125	0.000	0.500	2
7	0.150	0.000	0.500	2
8	0.175	0.000	0.500	2
9	0.200	0.000	0.500	2
10	0.225	0.000	0.500	2
11	0.250	0.000	0.500	2
12	0.275	0.000	0.500	2
13	0.300	0.000	0.500	2
14	0.325	0.000	0.500	2
15	0.350	0.000	0.500	2
16	0.375	0.000	0.500	2
17	0.400	0.000	0.500	2
18	0.425	0.000	0.500	2
19	0.450	0.000	0.500	2
20	0.475	0.000	0.500	2
21	0.500	0.000	0.500	2
22	0.525	0.000	0.500	2
23	0.550	0.000	0.500	2
24	0.575	0.000	0.500	2
25	0.600	0.000	0.500	2
26	0.625	0.000	0.500	2
27	0.650	0.000	0.500	2
28	0.675	0.000	0.500	2
29	0.700	0.000	0.500	2
30	0.725	0.000	0.500	2
31	0.750	0.000	0.500	2
32	0.775	0.000	0.500	2
33	0.800	0.000	0.500	2
34	0.825	0.000	0.500	2
35	0.850	0.000	0.500	2
36	0.875	0.000	0.500	2
37	0.900	0.000	0.500	2
38	0.925	0.000	0.500	2
39	0.950	0.000	0.500	2
40	0.975	0.000	0.500	2
41	1.000	0.000	0.500	2
42	1.000	0.025	0.500	2

43	1.000	0.050	0.500	2
44	0.975	0.050	0.500	2
45	0.950	0.050	0.500	2
46	0.925	0.050	0.500	2
47	0.900	0.050	0.500	2
48	0.875	0.050	0.500	2
49	0.850	0.050	0.500	2
50	0.825	0.050	0.500	2
51	0.800	0.050	0.500	2
52	0.775	0.050	0.500	2
53	0.750	0.050	0.500	2
54	0.725	0.050	0.500	2
55	0.700	0.050	0.500	2
56	0.675	0.050	0.500	2
57	0.650	0.050	0.500	2
58	0.625	0.050	0.500	2
59	0.600	0.050	0.500	2
60	0.575	0.050	0.500	2
61	0.550	0.050	0.500	2
62	0.525	0.050	0.500	2
63	0.500	0.050	0.500	2
64	0.475	0.050	0.500	2
65	0.450	0.050	0.500	2
66	0.425	0.050	0.500	2
67	0.400	0.050	0.500	2
68	0.375	0.050	0.500	2
69	0.350	0.050	0.500	2
70	0.325	0.050	0.500	2
71	0.300	0.050	0.500	2
72	0.275	0.050	0.500	2
73	0.050	0.050	0.500	2
74	0.225	0.050	0.500	2
75	0.200	0.050	0.500	2
76	0.175	0.050	0.500	2
77	0.150	0.050	0.500	2
78	0.125	0.050	0.500	2
79	0.100	0.050	0.500	2
80	0.075	0.050	0.500	2
81	0.050	0.050	0.500	2
82	0.025	0.050	0.500	2
83	0.000	0.050	0.500	2
84	0.000	0.025	0.500	2

85	0.100	0.002	0.063	0 electrode points
86	0.100	0.002	0.125	0
87	0.100	0.002	0.188	0
88	0.100	0.002	0.250	0
89	0.100	0.002	0.313	0
90	0.100	0.002	0.375	0
91	0.100	0.002	0.438	0

92	0.200	0.002	0.063	0
93	0.200	0.002	0.125	0
94	0.200	0.002	0.188	0
95	0.200	0.002	0.250	0
96	0.200	0.002	0.313	0
97	0.200	0.002	0.375	0
98	0.200	0.002	0.438	0

99	0.300	0.002	0.063	0
100	0.300	0.002	0.125	0
101	0.300	0.002	0.188	0
102	0.300	0.002	0.250	0
103	0.300	0.002	0.313	0
104	0.300	0.002	0.375	0
105	0.300	0.002	0.438	0

106	0.400	0.002	0.063	0
107	0.400	0.002	0.125	0
108	0.400	0.002	0.188	0
109	0.400	0.002	0.250	0
110	0.400	0.002	0.313	0
111	0.400	0.002	0.375	0
112	0.400	0.002	0.438	0

113	0.500	0.002	0.063	0
114	0.500	0.002	0.125	0
115	0.500	0.002	0.188	0
116	0.500	0.002	0.250	0
117	0.500	0.002	0.313	0
118	0.500	0.002	0.375	0
119	0.500	0.002	0.438	0

120	0.600	0.002	0.063	0
121	0.600	0.002	0.125	0
122	0.600	0.002	0.188	0
123	0.600	0.002	0.250	0
124	0.600	0.002	0.313	0
125	0.600	0.002	0.375	0
126	0.600	0.002	0.438	0

127	0.700	0.002	0.063	0
128	0.700	0.002	0.125	0
129	0.700	0.002	0.188	0
130	0.700	0.002	0.250	0
131	0.700	0.002	0.313	0
132	0.700	0.002	0.375	0
133	0.700	0.002	0.438	0

134	0.800	0.002	0.063	0
135	0.800	0.002	0.125	0
136	0.800	0.002	0.188	0
137	0.800	0.002	0.250	0
138	0.800	0.002	0.313	0
139	0.800	0.002	0.375	0
140	0.800	0.002	0.438	0

141	0.900	0.002	0.063	0
142	0.900	0.002	0.125	0
143	0.900	0.002	0.188	0
144	0.900	0.002	0.250	0
145	0.900	0.002	0.313	0
146	0.900	0.002	0.375	0
147	0.900	0.002	0.438	0

148	0.500 0.025 0.25 0 ghost node
149 0.500 0.024 0.25 0 ghost node refine point

0	no internal boundaries
0	no holes

1
1 0.25 0.025 0.25 2e-6 .005 .00005 zone* x y z maxvol real_cond imag_cond

1
'px'
0
<end file tank.cfg> this line is not included in tank.cfg